## Slide 1
LISA-like laser ranging for
GRACE follow-on
Daniel Schütze, Gunnar Stede, Vitali Müller,
Oliver Gerberding, Christoph Mahrdt, Benjamin Sheard, Gerhard Heinzel, and Karsten Danzmann
LISA Symposium, May 24, 2012

## Slide 2: Outline
Introduction
  Satellite gravimetry
  What is GRACE? What is GRACE follow-on (GFO)?
  Progress at AEI: Triple Mirror Assembly (TMA) and Optical Bench (OB)
Test setup for the TMA
OB prototype testing
Summary

## Slide 3: Satellite gravimetry
GFZ Potsdam
Mapping the global gravity field
  Often expressed as spherical harmonic expansion
  Static and dynamic components
  Geoscience (glacial/polar ice changes, solid earth deformation, hydrology)
Techniques
  Orbit determination and tracking
  Satellite-to-satellite tracking (SST)
  Gravity gradiometry
Recent gravity field satellites
  CHAMP (Germany)
  GRACE (US-German collaboration)
  GOCE (ESA)
GFZ

## Slide 4: What is GRACE?
CSR

## Slide 5: What is GRACE?
CSR

## Slide 6: What is GRACE?
CSR

## Slide 7: What is GRACE?
B. D. Tapley et al., “GRACE Measurements of Mass Variability in the Earth System”, Science 305, 503—505 (2004).
CSR

## Slide 8: What is GRACE follow-on?
Urgent continuation of GRACE data, launch in 2017
Use basically the same satellites, add Laser Ranging Instrument (LRI) as technology development
LRI offers additional data streams:
  LRI inter-satellite distance measurements can be compared to K-band ranging
  Satellite pointing information via Differential Wavefront Sensing (DWS)/Steering mirror control can be compared with star tracker data
CSR

## Slide 9: GRACE follow-on & LISA
CSR
 | LISA | GFO
Inter-satellite distance measurement | Heterodyne laser interferometry (receiver-transponder) with offset phase-locked lasers and phasemeter readout | 
Inter-satellite distance | 5 million km | ≈200 km
Orbit | Heliocentric (1 a.u.) | LEO (≈400 km)
Orbit environment | No atmospheric drag, stable thermal environment | Atmospheric drag, large thermal disturbances
Attitude and Orbit Control System | Drag-free using µN thrusters | Attitude control with magnetotorquers & cold gas thrusters
Measurement band | ≈mHz – Hz | 
Single-link noise | 12 pm/√Hz (× freq. dep.) | ≈50 nm/√Hz (× freq. dep.)
Telescope aperture diameter | 38 cm | ≈1 cm
Transmit beam waist radius | 17 cm | ≈2 mm
Transmit power | 1 W | ≈30 mW
Effective received power (at photodetector) | ≈100 pW | 
Maximum relative L.O.S. velocity | ±15 m/s | ≤ ±5 m/s (depending on orbits)

## Slide 10: Who is involved in GRACE follow-on?
CSR
Joint NASA/GFZ mission
Spacecraft built by Astrium
LRI has different contributions:
  AEI: Germany PI, instrument development and testing
  JPL: US PI, Laser Ranging Processor (LRP), frequency-stabilized lasers
  ANU: Triple Mirror Assembly (TMA)
  DLR: hardware contributions (photodiodes, electronics)
  Astrium: contributions to system engineering/ testing
  STI: instrument manufacturing

## Slide 11: What is GRACE follow-on?

## Slide 12: Triple mirror assembly
Lateral Transfer
Hollow Retroreflector™ from PLX

## Slide 13: Triple Mirror Assembly - basic properties
Place virtual intersection point inside accelerometer
Rotation around virtual intersection point preserves:
  round-trip pathlength d
  beams antiparallel
  impact parameter p
,

## Slide 14: Triple Mirror Assembly - coupling of displacement into length measurement
 | Dx | Dy | Dz
u | 0 | 0 | 0
v | 2Dxv | 0 | 2Dz
w | 2Dxw | -2Dy | 0
Linearize
dL = 2vDz – 2wDy
u
v
w

## Slide 15: Optical Bench

## Slide 16: Optical Bench - Differential Wavefront Sensing
Split photodetector results in a phase difference between the heterodyne signals proportional to wavefront tilt:
Quadrant photodetector allows the simultaneous measurement in two independent axes:

## Slide 17: Optical Bench - Differential Wavefront Sensing

## Slide 18: Optical Bench - Differential Wavefront Sensing
When spacecraft rotates the incoming beam is tilted relative to the local beam leading to a non-zero DWS signals, reduction of contrast and misaligned outgoing beam

## Slide 19: Optical Bench - Differential Wavefront Sensing
Appropriately feeding back the DWS signals to the steering mirror zeros the DWS signals and corrects the outgoing beam direction

## Slide 20: Optical Bench - Differential Wavefront Sensing
Appropriately feeding back the DWS signals to the steering mirror zeros the DWS signals and corrects the outgoing beam direction
Acquisition:
Poster by C. Mahrdt

## Slide 21: Triple Mirror Assembly test setup
x
z
y

## Slide 22: Triple Mirror Assembly test setup - lab picture

## Slide 23: Determine vertex/ point of minimal coupling of TMA
dL = 2v(Vz-PPz) – 2w(Vy-PPy)

## Slide 24: Determine vertex/ point of minimal coupling of TMA
dL = 2v(Vz-PPz) – 2w(Vy-PPy)

## Slide 25: Next step: Hexapod-independent coordinate frame

## Slide 26: Next step: Hexapod-independent coordinate frame
Ifocad-Simulations:
Poster by E. Kochkina

## Slide 27: Optical Bench prototype test setup

## Slide 28: Optical Bench prototype test setup - round-trip pathlength measurement
Demonstrates the inherent immunity of the racetrack design to Optical Bench motion in the round-trip pathlength measurement

## Slide 29: Optical bench prototype test setup - lab picture

## Slide 30: Optical bench prototype

## Slide 31: Optical bench prototype - DWS/Steering mirror closed-loop, DWS and length stability

## Slide 32: Next steps
Verify performance of Optical bench
Integrate Optical bench and Triple mirror assembly (will be delivered from ANU) in one setup

## Slide 33: Summary
GRACE follow-on will be a milestone as the first inter-satellite laser interferometer with many similarities to LISA
Work progress at AEI:
  Triple Mirror Assembly test setup: Determine vertex of TMA by rotating hexapod
  Optical Bench prototype: DWS with closed steering mirror loop established
Thanks for your attention!