## Slide 1: Possible Periodic Orbit Control Maneuvers for the LISA Mission
Peter L. Bender
JILA, University of Colorado and NIST
9th International LISA Symposium
May 21 – 25, 2012 Paris

## Slide 2: LISA Orbits with no Earth Perturbations
Arm length variations:
  D12 = √12 ea { 1 + 15/32 e cos(L-120°) + 1/32 e cos3L }
  D23 = √12 ea { 1 + 15/32 e cos L + 1/32 e cos3L }
  D31 = √12 ea { 1 + 15/32 e cos(L+120°) + 1/32 e cos3L }
For 1 x 106 km arm lengths:
  L = mean longitude of the antenna
  e = 1.93 x 10-3 ; a = 1 AU
  angle variations = 60° ± 0°.0898
  arm length variations = ± 965 km
Drift-away heliocentric orbits
2 year mission lifetime

## Slide 3: Arm Length Accelerations due to the Earth
Accelerations:
  23 = 2√3K cos2 L ; 12 = 2√3K cos2 (L – 120°) 31 = 2√3K cos2 (L + 120°)
For 1 x 106km arm length and 12° from Earth:
  K = 7.0 x 10-9m/s2
Leaving out the constant parts:
  23 = √3K cos 2 L 12 = √3K cos 2 (L – 120°) 31 = √3K cos 2 (L + 120°)

## Slide 4: Cancellation of Extra Arm Length Accelerations
Assume R1, R2, R3 are applied radial accelerations out from the center of the triangle for the 3 spacecraft to cancel one-half of the extra accelerations:
  R1 = K cos 2 L ; R2 = K cos 2 (L + 120°)
  R3 = K cos 2 (L - 120°)
Assume similar applied tangential accelerations T1, T2, T3 in the clockwise direction around the center of the triangle:
  T1 = K sin 2 L ; T2 = K sin 2 (L + 120°)
  T2 = K sin 2 (L - 120°)
A simulation of this approach is needed. However, it appears that these accelerations would cancel out the extra accelerations.

## Slide 6: One Mission Option for Cancellation
Drift-away orbit:
  6° per year drift rate
  12° from Earth initially. (However, some extra ΔV is required to achieve this.)
At 12° from Earth:
  K = 7.0 x 10-9 m/s2
  Over 6 days, ΔV = 3.6 x 10-3 m/s
Assume 80 micro-N thrust is available in each in-plane direction, and 70 micro-N can be used for orbit maintenance, with 600 kg spacecraft:
  8.6 hr of thrust is needed every 6 days to achieve ΔV cancellation initially
  6.1 hr is needed every 6 days after 3 month commissioning period
  2.6 hr is needed every 6 days after 1 year

## Slide 7: Conclusions
Orbit control to prevent the increase of angle variations beyond 0.°1 for a LISA-type mission with 106 km arm lengths appears to be feasible. This would considerably simplify the in-field guiding system for compensating for the angle changes.
If 80 micro-N maximum thrust is available in both the radial and transverse directions, and a drift-away orbit that starts 12° from the Earth can be used, the maximum lost time for science after the commissioning period would be about 4%.
The maximum voltage applied to the GRS electrodes during thrusting would be about 40 V RMS, which is within the “wide range” of voltages available on the GRS.